## Slide 1: SLAC Site Report
Les Cottrell SLAC, May 5, 2017
ESCC meeting LBNL,

## Slide 2: Life-cycle today
Network
Core, was 11 years old
  Upgrade completed March 31st 2017 – Cisco 7710s
  100Gbps interconnects, 40Gbps support
Border 11 years old
  Requested funding for two Cisco 7700s
  Two * 100Gbps to ESnet
    Preparation for LCLS-II etc.
Distribution
  Requested funding
Edge/buildings (oldest 11 years old)
  Requested funding for 1st 5 building floors
  Choice based on age and importance of building

## Slide 3: Life cycle plan
Lease vs Buy
Follow industry practice for hardware lifecycle = 5 years
    Supported/patched equipment is a must for cyber aspects
    Expect ~15% reduction in footprint every 5 years
  Virtualized and consolidated datacenter reducing footprint
    Less servers needing more bandwidth (10G/40G) – Number of servers reduced by 15% every 5 years
  More services moving to the cloud (O365, AWS, Azure…)
    Less servers on premise. Less horizontal traffic, more vertical. Border/filtering/inspection more important.
  Campus wireless growth reducing need for wire
    VoIP strategy will play a key role
      Cell/Wireless phones/softphones phasing out wired phones
    Estimated trends: +20 access points/year, -5 campus switches/year

## Slide 4: Mobility
WiFi
  Horizontal cable reduction
  802.11ac
  External, between building and trailer
Cellular
  Carriers with macro sites at SLAC: AT&T, Verizon, Sprint, T-Mobile
  Underground
    DAS in about 6 locations, typical cost about $10K
    In occasional radiation areas looking at WiFi

## Slide 5: Cyber-security
Hardened border
  PANs ingress and egress, ~80 apps allowed
  Push back from users, in particular science
  Lot of outreach/negotiation, tuning
  Many incidents of unexpected denials
    Painful to user but not widespread
    Treat as emergency, fix then get permission etc
Bifurcation into low and moderate based on host (from NetDB)
MFA
  DuO and smartphones, Ubi-keys
PIV-I
Next
  Cloudpath

## Slide 6: Cyber Federated Model
CFM and blocks
  Border peers with rtr-block
  For suspect sites border sends to rtr-block which black-holes
  Database updates rtr-block tables
  Huge number of ‘high’severity recommendations from CFM
  Overflows (60K) the table in the border router
    Border stops sending to rtr-block, so now open
    Get warnings, manually kill table
  Working on better solution
    Don’t accept blocks from selected CFM contributors
    Upgrade of border gives three times table space.
    Investigate CFM from CFM team.
    Utilize confidence and severity
    Look at github UIUC/NCSA to run a black hole/null-router on a Linux box feeding routes via BGP into fabric
    Aggregate CIDR blocks

## Slide 7: Team
New architect
  Mark Foster ex NASA/Ames
New Engineer
  Andy Deshmukh
Les closing in on retirement

## Slide 8: Questions