## Slide 1: July 25, 2016
Ben Reese
Firmware Development Overview
TID-AIR Electronics Systems

## Slide 2: What will be covered
VHDL language overview
SLAC VHDL coding style
Available VHDL libraries (StdLib)
  Building blocks
  AXI Infrastructure
  Peripheral interfaces

## Slide 3: VHDL
SLAC firmware development is almost exclusively in VHDL.
Many aspects of VHDL are annoying
  Verbosity
  Pedantic typing
  Array types must be manually declared
But some features are really great
  Record types
  Procedures
All code is written to VHDL-93 standard.
  We use entity instantiations so that ‘components’ don’t need to be declared.
  VHDL-2008 fixes a lot of VHDL annoyances
  Has been official for 8 years now.
  We would love to use it
  Support in major vendor toolchains (Xilinx, Synopsys) still half-assed at best.
  Hopefully we can migrate to it someday when decent tool support exits.

## Slide 4: VHDL Coding Style - Basics
Entities are named in CamelCase style with leading word capitalized.
entity SimpleCounter is ...
Entity and Architecture always go in the same file.
  Synthesizable architectures should be named ‘rtl’
  Simulation only architectures should be named ‘sim’
  Not a hard rule. We don’t use configurations so it doesn’t really matter what the architecture names are.
Packages are the same but end in *Pkg
package Crc32Pkg is ...
File name should mirror entity or package name with .vhd extension.
Constants are named in all caps with underscores and end in *_C.
constant MAX_COUNT_C : integer := 24;
Entity generics are also all caps but end in *_G
entity SimpleCounter is
generic (
MAX_COUNT_G : integer := 24;
...
Ports and signals are camelCase with leading word not capitalized.
signal currentCount : std_logic_vector(7 downto 0);

## Slide 5: VHDL Coding Style
Type definitions are CamelCase and end in *Type
State machine enumerations named like constants but end in *_S
type StateType is (
IDLE_S, START_S, ACTIVE_S, END_S);
Misc
  Use spaces and not tabs
  Use a code formatter (emacs has a good one).

## Slide 6: VHDL Coding Style
All SLAC VHDL code uses a “two-process” coding style.
Each module has:
  One combinatorial process that describes all the logic.
  One (boilerplate) sequential process that assigns the combinatorial outputs to registers on the rising edge of each clock.
Record types are used extensively
  Record in each module defines all the registers.
  Records in Packages define port IO.
    Don’t have to fix every instantiation when a port map changes. Just update the record and everything still works!
Functions and procedures also used extensively.
Code in this style is much more readable and easier to understand. Module algorithms become much clearer.
See http://www.gaisler.com/doc/vhdl2proc.pdf for a full write-up of the benefits of this style.

## Slide 7: Coding Style Example – Simple Counter
entity Counter is
generic (
TPD_G : time := 1 ns); -- Simulated propagation delay
port (
clk : in sl;
rst : in sl;
max : in slv(7 downto 0);
count : out slv(7 downto 0);
rollover : out sl);
end entity Counter;
architecture rtl of Counter is
-- Record containing all register elements
type RegType is record
count : slv(7 downto 0);
rollover : sl;
end record RegType;
-- Initial and reset values for all register elements
constant REG_INIT_C : RegType := (
count => (others => '0'),
rollover => '0');
-- Output of registers. (The Q output)
signal r : RegType := REG_INIT_C;
-- Combinatorial input to registers (The D input)
signal rin : RegType;
begin
-- Boilerplate sequential process
-- Assign rin to r on rising edge of clk to create registers
seq : process (clk) is begin
if (rising_edge(clk)) then
r <= rin after TPD_G;
end if;
end process seq;
-- Main module logic
-- Generates rin based on r and any module inputs
comb : process (max, r, rst) is
variable v : RegType;
begin
-- Initialize v with current value of all registers
v := r;
-- Set register values for next rising edge
v.count := r.count + 1;
v.rollover := '0';
-- Override above assignments when max reached
if (r.count = max) then
v.count := (others => '0');
v.rollover := '1';
end if;
-- Synchronous reset
-- Override all above assignments and apply init values
if (rst = '1') then
v := REG_INIT_C;
end if;
-- Assign final state of local variable to rin signal
-- Registers will assume these values on next rising edge
rin <= v;
-- Assign registered signals to outputs
count <= r.count;
rollover <= r.rollover;
end process comb;
end architecture rtl;

## Slide 8: Packages
Packages are very useful for sharing constants, typedefs, functions and procedures.
With the “two-process” coding style, functions and procedures become very easy to use.
  Can abstract complex logic to avoid code repetition.
  Procedures used when a logic block has more than one output, or needs to read and update a variable.

## Slide 9: Procedure Example
procedure updateCount(
v : inout RegType;
max : in slv(7 downto 0)) is
begin
if (v.count = max) then
v.count := (others => ‘0’);
v.rollover := ‘1’;
else
v.count := v.count + 1;
v.rollover := ‘0’;
end if;
end procedure;
Comb : process (r, max) is
variable v := RegType;
begin
v := r;
updateCount(v);
rin <= v;
end process;

## Slide 10: The SLAC StdLib
StdLib contains many useful modules for firmware development
  Generic building blocks
    Clock Synchronization
    RAMs
    FIFOs
  AXI Bus infrastructure
    AXI-Lite
    AXI-Stream
    AXI DMA
  Peripheral Interfaces (with AXI endpoint wrappers)
    I2C
    SPI
Designed to be easier to use and configure than Xilinx IP Cores.

## Slide 11: StdLib File Structure
StdLib sub-libraries
  general
    rtl – Synthesizable modules
  sync
  ram
  fifo
  axi
  srp
  spi
  i2c
  uart
  xilinx7
  xilinxUltraScale
  build – Build system for Xilinx. Covered in a later talk

## Slide 12: StdLib – general/rtl/StdRtlPkg.vhd
StdRtlPkg is the most important file in the library
Defines types, functions and procedures that are so useful that every module you make will ‘use’ it.
  use work.StdRtlPkg;
-- Typing std_logic(_vector) is annoying
subtype sl is std_logic;
subtype slv is std_logic_vector;
-- Declare arrays of built in types
type IntegerArray is array (natural range <>) of integer;
type NaturalArray is array (natural range <>) of natural;
type PositiveArray is array (natural range <>) of positive;
type RealArray is array (natural range <>) of real;
type TimeArray is array (natural range <>) of time;
type BooleanArray is array (natural range <>) of boolean;

## Slide 13: StdRtlPkg – Other useful functions
StdRtlPkg also provides several convince functions:
  log2() – Find number of bits needed to hold a number
  Unary reduction
    uOr(), uAnd(), uXor() – Called on ‘slv’ to reduce to ‘sl’.
  toBoolean(), toSl() – Convert between ‘sl’ and boolean.
  grayEncode() – generate gray code for an slv
  ite() – Ternary logic operator like Verilog and C have.
    Can be used to conditionally assign constant values
constant TEST_C : integer := ite(GENERIC_G = 7, 0, 1);
    This is really useful!
    Can be cascaded for complex constant assignments
    Can assign boolean, sl, slv, bit_vector, character, string, integer, real and time types.
    Developer can create additional overloads of ite() for custom types.

## Slide 14: General – Available Packages and Modules
ArbiterPkg – Defines functions and procedures to facilitate implementation of round-robin arbiters
TextUtilPkg – Useful functions writing output to files.
Crc32 – CRC32 checksum generator. Several implementations available.
8B10B – Encoder and decoder
Heartbeat – Drive a heartbeat LED.
ClockDivider – Divide a clock by a programmable amount, with programmable duty cycle.
SlvDelay – Create long register delay chains. Can infer SRL primitives for Xilinx devices.

## Slide 15: StdLib - Synchronization
Proper synchronization of signals between clock domains is a critical aspect of any firmware design.
Most people do it wrong.
  Consequences will never be seen in simulation.
  Will show up intermittently in deployed design.
StdLib has several modules to properly synchronize signals between clock domains.
Many synthesis tools allow attributes to be specified on synchronization registers.
  Synchronization chains should be placed in same slice with no logic between each stage.
  StdLib Sync modules declare all the necessary attributes for several different synthesis tools.
    Vivado, ISE, Synplify, Quartus

## Slide 16: Synchronization Modules
Synchronizer – Syncrhonize a 1 bit signal (sl) through 2 or more flip flops.
SynchronizerVector – Synchronize an array (slv) through 2 or more flip flops.
  Used for arrays of individual status bits
  Not for multi-bit values (data busses, etc)
SynchronizerFifo – Use a small asynchronous FIFO to safely synchronize data busses between clock domains.
RstSync – Special synchronizer for resets. Output has asynchronous rising edge and synchronized falling edge.
SyncrhonizerOneShot – Can catch a pulse on the input side that is faster than the clock being synchronized to. Output single pulse on synchronized domain in response.

## Slide 17: StdLib – RAM Modules
RAM modules are intended as a replacement for Xilinx IP core generated Block RAMs and Distributed RAMs.
Generics control data width and address size.
Generics control Block RAM of Distributed (LUT) RAM.
Generics can even allow byte level write enables and infer built in BRAM output registers.
Under the hood, VHDL code is specifically formatted so that RAMs can be inferred.
  This makes them portable between Xilinx, Altera, etc.

## Slide 18: RAM modules
Note: All dual-port RAMs allow for asynchronous clocks on each port.
TrueDualPortRam – RAM with two ports, each of which is readable and writable.
DualPortRam - One port readable and writable. One port read only.
SimpleDualPortRam – One port write only. One port read only. Useful for FIFOs. Better resource optimization when used as Xilinx BRAMs.
QuadPortRam – One read/write port. Three read only ports. Only available as LUT RAM.
SinglePortRam – Instantiate any of the dual port RAMs and don’t hook up one of the ports. Synthesis will optimize it out.

## Slide 19: FIFOs
Intended as replacements for Xilinx FIFO IP cores.
Generics allow simple configuration of:
  Data width
  Depth
  Synchronous or Asynchronous
  First-word-fall-through
  BlockRAM or LUTRAM underneath
  Programmable Full threshold
  Programmable Empty threshold
Full featured with all the signals you expect:
  empty, valid (not empty), almost_empty, prog_empty
  full, not_full, almost_full, prog_full
  data_count
Don’t hook up signals you don’t need and they will optimize out.

## Slide 20: FIFO Modules
Fifo – Main FIFO module that should usually be instantiated. Can create synchronous or asynchronous FIFO.
FifoCascade – Extra generics available to create a cascading series of FIFOs. Allows for larger FIFOs to be built while easing timing closure.
FifoMux – (Poorly named). FIFO with asymmetric write and read data widths.

## Slide 21: AXI Infrastructure
AXI protocols (AXI, AXI-Lite, AXI-Stream) form the system level backbone of SLAC firmware designs.
The key features of the AXI protocol are:
  Separate address/control and data phases
  Support for unaligned data transfers, using byte strobes
  Uses burst-based transactions with only the start address issued
  Separate read and write data channels
  Support for issuing multiple outstanding addresses
  Support for out-of-order transaction completion
  Permits easy addition of register stages to provide timing closure.
  Supports multiple masters simultaneously accessing multiple slaves.
The AXI-Lite protocol is a subset of AXI that facilitates communication with simpler control register style interfaces within components.
  Fixed 32-bit address, 32-bit data
  Disabled support for burst transactions.
  Disabled support for multiple outstanding transactions
  Disabled support for out-of-order transactions
  If you want to make your firmware registers accessible by software, you need to make an AXI-Lite interface to them.

## Slide 22: AXI-Lite Bus record types - StdLib/axi/AxiLitePkg.vhd
type AxiLiteReadMasterType is record
-- Read Address channel
araddr : slv(31 downto 0);
arprot : slv(2 downto 0);
arvalid : sl;
-- Read data channel
rready : sl;
end record;
type AxiLiteReadSlaveType is record
-- Read Address channel
arready : sl;
-- Read data channel
rdata : slv(31 downto 0);
rresp : slv(1 downto 0);
rvalid : sl;
end record;
type AxiLiteWriteMasterType is record
-- Write address channel
awaddr : slv(31 downto 0);
awprot : slv(2 downto 0);
awvalid : sl;
-- Write data channel
wdata : slv(31 downto 0);
wstrb : slv(3 downto 0);
wvalid : sl;
-- Write ack channel
bready : sl;
end record;
type AxiLiteWriteSlaveType is record
-- Write address channel
awready : sl;
-- Write data channel
wready : sl;
-- Write ack channel
bresp : slv(1 downto 0);
bvalid : sl;
end record;

## Slide 23: AXI-Lite Crossbar – StdLib/axi/AxiLiteCrossbar
AXI busses need to be fanned out to each Slave by an Interconnect/Crossbar
AxiLiteCrossbar.vhd is a very versatile module for doing this.
Also allows multiple masters to access multiple slaves
Number of Masters ports and Slave ports configured by generic
Confusing terminology
  “Master” and “Slave” are from the crossbar port perspective
  “Master” ports attach to downstream slave modules
  “Slave” ports attach to upstream masters
Generics configure number of master and slave ports, and the address range of each master port.
AxiLiteCrossbars are often cascaded down through a firmware hierarchy
AxiLiteCrossbar
Slave Module A
0xA0000000-
0xA000FFFF
Slave Module B
0xA0010000-
0xA00100FF
Slave Module C
0xA0010100-
0xA00101FF
Slave Module D
0xA0020000-
0xA002FFFF
S AXIL BUS 0
S AXIL BUS 1
S AXIL BUS 2
S AXIL BUS 3
Slave 0
Master 1
Master 3
Master 2
AxiLiteMaster
M AXIL BUS
Master 0

## Slide 24: AXI-Lite Endpoint Example
AxiLitePkg.vhd has many helpful functions and procedures for adding AXI-Lite registers to your module.
We’ve abstracted away the hairy details of the AXI-Lite bus signaling and address decoding into a set of procedure calls.
entity AxiLiteModule is port (
axiClk : in sl;
axiRst : in sl;
axiReadMaster : in AxiLiteReadMasterType;
axiReadSlave : out AxiLiteReadSlaveType;
axiWriteMaster : in AxiLiteWriteMasterType;
axiWriteSlave : out AxiLiteWriteSlaveType;
end AxiLiteModule;
architecture rtl of AxiLiteModule is
constant CONSTANT_C : slv(31 downto 0) := X"01234567";
type RegType is record
register0 : slv(31 downto 0);
register1 : slv(7 downto 0);
register2 : slv(15 downto 0);
axiReadSlave : AxiLiteReadSlaveType;
axiWriteSlave : AxiLiteWriteSlaveType;
end record RegType;
[...]

## Slide 25: AXI-Lite Endpoint Example Cont.
comb : process (r, axiRst, axiReadMaster, axiWriteMaster) is
variable v : RegType;
variable axilEp : AxiLiteEndpointType;
begin
v := r;
[...]
axiSlaveWaitTxn(axilEp, axiWriteMaster, axiReadMaster, v.axiWriteSlave, v.axiReadSlave);
axiSlaveRegisterR(axilEp, X"00", 0, CONSTANT_C);
axiSlaveRegister(axilEp, X"04", 0, v.register0);
axiSlaveRegister(axilEp, X"08", 0, v.register1);
axiSlaveRegister(axilEp, X"08", 8, v.register2);
axiSlaveDefault(axilEp, v.axiWriteSlave, v.axiReadSlave);
[...]
end process;
Notes:
All address offsets should be the same width
  Multiples of 4 bits preferred
Byte addressing on 32-bit values means that address offsets should always be multiples of 4.
  X”001”, X”002” are not a valid offsets.
See StdLib/axi/rtl/AxiVersion.vhd for a more complete example.

## Slide 26: AxiLite Dual Port RAM
AxiDualPortRam is a useful memory bridge between AXI-Lite (usually driven by software) and a firmware module logic.
It creates a RAM with an AXI-Lite interface on one port and a generic RAM interface on the other.
Like other RAMs, generics can configure:
  BRAM or LUTRAM
  Data width
  Address size
Can also make either side read-only, and use asynchronous clocks on each side.

## Slide 27: Other AXI-Lite modules
AxiLiteAsync – Transfer an AXI-Lite bus across asynchronous clock domains.
AxiLiteEmpty – Blank endpoint that responds to all accesses with 0 or error depending on generics. Typically used as an endpoint placeholder.
AxiLiteToDrp – Translates AXI-Lite accesses into Xilinx DRP bus for reprogramming FPGA primatives.
AxiLiteToIpBus – Bridge an AXI-Lite bus onto an IPBus
IpBusToAxiLite – Bridge an IPBus onto an AXI-Lite bus.

## Slide 28: AxiDualPortRam
entity AxiDualPortRam is
generic (
TPD_G : time := 1 ns;
BRAM_EN_G : boolean := false;
AXI_WR_EN_G : boolean := true;
SYS_WR_EN_G : boolean := false;
COMMON_CLK_G : boolean := false;
ADDR_WIDTH_G : integer range 1 to (2**24) := 5;
DATA_WIDTH_G : integer := 32);
port (
-- Axi Port
axiClk : in sl;
axiRst : in sl;
axiReadMaster : in AxiLiteReadMasterType;
axiReadSlave : out AxiLiteReadSlaveType;
axiWriteMaster : in AxiLiteWriteMasterType;
axiWriteSlave : out AxiLiteWriteSlaveType;
-- Standard Port
clk : in sl := '0';
en : in sl := '1';
we : in sl := '0';
rst : in sl := '0';
addr : in slv(ADDR_WIDTH_G-1 downto 0) := (others => '0');
din : in slv(DATA_WIDTH_G-1 downto 0) := (others => '0');
dout : out slv(DATA_WIDTH_G-1 downto 0));
end entity AxiDualPortRam;

## Slide 29: AXI-Stream
Like AXI-Lite, AXI4-Stream is a subset of AXI protocol.
It is designed for high-speed streaming data.
It is quite useful in firmware applications for passing data around.
  RCE DMA ports use AxiStreams.
Master driven signals:
  TVALID – Transaction is valid
  TDATA – Data to transfer. 8-128 bits wide
  TLAST – Marks end of frame
  TUSER – Optional sideband data. Up to 8 bits per TDATA byte
  TKEEP – Marks which data bytes are valid
  TDEST – Optional routing information
  TID – Optional source information
  TSTRB – Marks positional data bytes (not often used)
Slave driven signal:
  TREADY – Transaction received.
Data transactions take place when TVALID and TREADY are both high.
Frames consist of multiple transactions with TLAST high on last transaction of frame.

## Slide 30: StdLib/axi/rtl/AxiStreamPkg.vhd
AxiStreamPkg.vhd defines record types for AXI-Streams.
All SLAC AxiStream modules use these records in their ports
Port widths are defined at maximum width (128 data bits)
  AxiStreamModules are passed an AxiStreamConfigType that specifies:
    Data width
    Sideband user bits
  Unused record bits are ignored an optimized out
type AxiStreamMasterType is record
tValid : sl;
tData : slv(127 downto 0);
tStrb : slv(15 downto 0);
tKeep : slv(15 downto 0);
tLast : sl;
tDest : slv(7 downto 0);
tId : slv(7 downto 0);
tUser : slv(127 downto 0);
end record AxiStreamMasterType;
type AxiStreamSlaveType is record
tReady : sl;
end record AxiStreamSlaveType;
type AxiStreamCtrlType is record
pause : sl;
overflow : sl;
idle : sl;
end record AxiStreamCtrlType;
type AxiStreamConfigType is record
TSTRB_EN_C : boolean;
TDATA_BYTES_C : natural range 1 to 16;
TDEST_BITS_C : natural range 0 to 8;
TID_BITS_C : natural range 0 to 8;
TKEEP_MODE_C : TkeepModeType;
TUSER_BITS_C : natural range 0 to 8;
TUSER_MODE_C : TUserModeType;
end record AxiStreamConfigType;

## Slide 31: AxiStreamFifo – StdLib/axi/rtl/AxiStreamFifo.vhd
The AxiStreamFifo block is used extensively with AXI-Streams.
It can be configured to perform all of the following functions, either all together or separately:
  Buffering
    Arbitrary sized buffers implemented with BRAM or LUTRAM FIFOs
    Optional Frame mode:
      Wait until a whole frame is in the buffer before sending it out the other side
  Synchronization
    Synchronize a stream across clock domains
  Bus resizing
    Resize stream data width to be wider or narrower.
    Example: 32 bits up to 128 bits.
    Example: 64 bits down to 8 bits.

## Slide 32: AxiStreamMux - AxiStreamDemux
AxiStreamMux is used to combine multiple streams onto a single channel.
  Once combined, the TDEST field is used to indicate the stream source
  Uses round-robin arbitration.
  Up to 16 streams can be combined.
  Beyond 16 the arbitration logic gets large
  Can cascade muxes if more streams need to be combined.
AxiStreamDemux is used to fan a stream out to multiple destinations based on the TDEST field.
  Module generics take a “route table” that specifies which TDESTs go to which output ports.

## Slide 33: Simple AxiStream example
User Application
Example of DMA streams fanning out to multiple PGP links.
Note that all SLAC developed link interface modules such as PGP and Ethernet use AxiStreams for their IO.
DMA
Engine
AxiStream
Mux
4:1
AxiStream
Demux
1:4
PGP 0
TX
RX
PGP 1
TX
RX
PGP 2
TX
RX
PGP 3
TX
RX
AxiStreamFifo
16:64
AxiStreamFifo
16:64

## Slide 34: SRP – Streaming Register Protocol
It is often necessary to send register access requests over a streaming link.
  Could include PGP, Ethernet, etc.
  These modules provide an AxiStream interface.
SLAC has specified a common streaming data format for register access called Streaming Register Protocol (SRP)
Frame format specifies locations for address, data, opcode, etc.
The StdLib contains modules for converting SRP formatted AxiStreams into AxiLite transactions and vice-versa.
Software drivers exist for sending SRP formatted frames over PGP and Ethernet to hook in to firmware registers.

## Slide 35: Typical SRP Use
Software
UDP Link
Firmware
Ethernet
UdpEngine
TX
RX
AxiStream
AxiStream
SrpToAxiLite
AxiLiteBus
AxiLite
Crossbar
AxiLiteBus
AxiLiteBus
AxiLiteBus
AxiLiteBus
Fanout to local modules
This is how standalone FPGA board typically tie in to software for register access

## Slide 36: I2C
Several I2C modules are available that allow firmware to attach to virtually any I2C peripheral.
Axi2cRegMaster – Maps one or more peripherals on an I2C bus into the AxiLite address space.
  Supports 7 and 10 bit device addresses
  Clock stretching
  Multiple address and data sizes in peripheral chip
  Big or little endian register access in peripheral
  All configurable for each peripheral on an I2C bus
I2cMaster, I2cRegMaster – Low level modules for I2C access. AxiI2cRegMaster is built on these.
I2cRegSlave – Allows firmware to function as a slave on an I2C bus.

## Slide 37: SPI
As with I2C, StdLib contains modules for SPI bus interfaces.
SpiMaster – Generic SPI bus master. Configurable word size. Sends and receives one word at a time on SPI bus.
AxiSpiMaster – Can map configuration registers of most SPI peripheral onto an AXI-Lite bus.
SpiSlave – Allows firmware to tie in as a slave on a SPI bus. Receives and sends one word at a time at the direction of a bus master.

## Slide 38: Conclusion
We’ve created a great infrastructure for developing firmware in VHDL.
We encourage you to use it!
This talk only scratched the surface of the available modules.
  We also have a whole Ethernet/UDP firmware stack.
  For RCE development, there is a nice DMA engine.
  Codebase will soon be migrated to GIT and hosted on Github for easy access.
  Documentation with Doxygen is also in the works.