## Slide 1: Abstraction Layer, 6x6 and HLO (Oh, my!)*
5June2020
* Apologies to Frank Baum

## Slide 2
Linac Sec. | V0 (MV) | j (deg) | Ave. Acc. Grad.* (MV/m) | No. Cryo Mod’s | No. Avail. Cav’s | Spare Cav’s | Cav’s per Amp.
L0 | 100 | ** | 16.3 | 1 | 8 | 0 | 1
L1 | 231 211 | -24.9 -12.7 | 14.8 13.6 | 2 | 16 | 1 | 1
HL | -60 -64.7 | -172.5 -150 | 12.4 13.4 | 2 | 16 | 2 | 1
L2 | 1479 1446 | -32.3 -21.0 | 15.8 15.5 | 12 | 96 | 6 | 1
L3 | 2538 2437 | 10 | 16.3 15.7 | 20 | 160 | 10 | 1
100pC, Elegant, BC1 R56= -53mm, BC2 R56= -45mm
NEW! Hot off the presses! Note changes to the chirp phases and the higher average cavity gradients in L1B, L2B and L3B
Old values in red

## Slide 3: High level PVs in Abstraction Layer for 6x6 FBCK Using L1B as an example
L1Eᵩ-
L2Eᵩ+
L2Eᵩ-
L3Eᵩ+
L3Eᵩ-
L1CHRPOFF
L1Eᵩ+
L2CHRPOFF
L3CHRPOFF
Value written to the LEM Phase of cavity 1 of CM02 would be:
ACCL:L1B:0210:PLEM (?) = L1CHRPDES + L1Eᵩ+
L1Eᵩ+ is calculated phase change to correct BPM offset in BC1
L1CHRPOFF is phase of chirp in L1B, -24.9°, adjusted in feedback to reach Ibunch or σz.
L1BFF is L1B Amplitude Fudge Factor to match linac section energy to BC1 applied to all cavities.
L1BFF
L2BFF
L3BFF
L0Eᵩ-
L0Eᵩ+

## Slide 4: HLO (Heat Load Optimization) and 6x6 FBCK
Heat Load Optimization, HLO, to optimize gradients for heat for cavities in the section.
  HLO has to calculate total required amplitude for the linac section from ∑(ADES). When do we use manual over write of PV to set linac section Amp?
Optimized cavities’ ADES are sorted from highest to lowest. Alternating entries are assigned to phase+ and phase- arrays in 1-2-1 order for use by other HLAs
HLO calculates ∑ADES of the cavities and passes value to PV for use by 6x6 FBCK.
6x6 FBCK adjusts both the Eᵩ and φchirp PVs for the three linac sections.
E = ∑((ADES)-(ADES Energy FBCK))* cos(φchirp) + ∑(ADES Energy FBCK)cos(φChirp)cos(Eᵩ1)
  Eᵩ2 = cos-1(cosEᵩ1 - ∆E / ∑(ADES Energy FBCK)), where
      Eᵩ1 is initial phase of energy feedback
      ∆E is amplitude of energy error at diagnostic
      ∑(ADES Energy FBCK) is sum of energy feedback cavities ADES
      Eᵩ2 is phase of energy feedback to correct energy offset in diagnostic
    ∆ φchirp  ∆Bunchlength or ∆Ibunch after compressor
Linac Sec. | No. Cryo Mod’s | No. Avail. Cav’s | Spare Cav’s | Chirp Cavs | Energy Feedback Cavities Eᵩ+, Eᵩ-
L0 | 1 | 8 | 0 | - | 2
L1 | 2 | 16 | 1 | ALL | 12
HL | 2 | 16 | 2 | - | -
L2 | 12 | 96 | 6 | ALL | 80
L3 | 20 | 160 | 10 | - | 128

## Slide 5: L1B Example
E Phase +
E Phase -
∑(ADES) = 231.9 MV
∑(ADES) for Energy FBCK = 186.7 MV
Energy Feedback range = 1.2%
HLO’d
L1B Sorted by ADES
ADES | Cavity
15.4 | 0210
15.4 | 0220
15.8 | 0230
15.7 | 0240
15.9 | 0250
15.5 | 0260
15.4 | 0270
15.4 | 0280
ADES | Cavity
15.2 | 0310
15.4 | 0320
15.6 | 0330
15.6 | 0340
15.2 | 0350
14.9 | 0360
15.5 | 0370
OFF | 0380
Initial
Initially, the chirp phase is 24.9° and ∑(ADES) is 231.9 MV. BUT,
Cavity 0360 is tripping >14.7 MV. OPS Max AMP is changed to 14.6 and L1B is re-HLO’d
ADES | Cavity
15.4 | 0210
15.4 | 0220
15.8 | 0230
15.7 | 0240
15.9 | 0250
15.5 | 0260
15.5 | 0270
15.4 | 0280
ADES | Cavity
15.4 | 0310
15.4 | 0320
15.6 | 0330
15.6 | 0340
15.2 | 0350
14.6 | 0360
15.5 | 0370
OFF | 0380
15.9 | 250
15.8 | 230
15.7 | 240
15.6 | 330
15.6 | 340
15.5 | 260
15.5 | 270
15.5 | 370
15.4 | 210
15.4 | 220
15.4 | 280
15.4 | 310
15.4 | 320
15.2 | 350
14.6 | 360
15.9 | 250
15.6 | 330
15.6 | 340
15.5 | 370
15.4 | 210
15.4 | 310
15.8 | 230
15.7 | 240
15.5 | 260
15.5 | 270
15.4 | 220
15.4 | 280
First 12 cavities sorted into Energy feedback phase+ and phase- arrays running at +/-10° from chirp φ

## Slide 6: Abstraction Layer in the Middle
Abstraction layer applies PVs for phases for energy feedback to individual cavities using labels from arrays generated by HLO
Abstraction layer applies PVs for phases for linac section chirp to all cavities in each linac section
Abstraction layer applies any other Gang phase values to groups of cavities
Abstraction layer compares optimized ADES or Operator input to the cavity Amplitude maximum, SRF, RF and OPS, and pushes the lessor values to LLRF for each cavity.
LLRF for 1 cavity
OPS Console
Amp
φ
Optimized
ADES
Max gradient
L.T.E.
Energy feedback φ
Chirp φ
Amp
φ
Abstraction Layer
Fancy phase Control
HLO optimizer
[Eᵩ+ Array]
[Eᵩ- Array]
Cavity in
Eᵩ+ Array?
Cavity in
Eᵩ- Array?
Y
Y

## Slide 7: Step by step re-HLO of Linac Section
If not already done, stop beam from injector
Stop 6x6 Feedback so after re-HLO it gets new value for Summed amplitude for energy feedback cavities
Update OPS Max gradients to reflect cavities which are to be turned down
Run HLO to optimize amplitude vs heat in linac section being re-optimized
  Calculate ∑(ADES) for linac section being optimized, this is integrated gradient required from the linac section
  Generate new, optimized cavity ADES less than cavity amplitude maximums
  Generate new Eᵩ+ and Eᵩ- arrays for energy feedback
  PUT new ADES values to cavities and turn cavities on
Pause feedbacks downstream of linac section being HLO’d so they don’t run away when beam is first restored.
Check that re-HLO’d cavities are running in SELAP at new amplitudes.
Restore beam in 1 Hz mode.
Turn on energy and chirp feedback in section under test.
  Watch that beam position at BPM in dispersive region moves to nominal orbit.
  Watch that bunchlength/peak current/ chirp phase come back to pre-HLO values.
Turn on down stream feedbacks.
Process is complete

## Slide 8: Details, always Details
‘GOLD’ phases are in the LLRF as ‘PREF’ PV. At what point in commissioning do we push values to those PVs?
Do we need to rewrite the 6x6 Feedback for differing dispersions, precision of new LLRF, etc? Is that Yuantao or Tim?
Should operator displays show amplitude and phase values written to LLRF or values input to abstraction layer?
Should Operator screens read actual readbacks or should abstraction layer invert process for readbacks?